## Slide 1: RF-based Device-free Gesture recognition and Motion Tracking
Ghufran
Swadhin

## Slide 2: Existing Techniques
Imaging based
  Pros
    Fine-grained tracking
    Multi-object tracking
    H/W abundant
  Cons
    Compute heavy
    require LOS (Occlusion)
    Privacy issues
Acoustic
  Pros
    Low on computation (Software based)
    No external hardware
    Good single object tracking
  Cons
    Limited bandwidth
    Human Irritation
    Specially modulated sound wave (FMCW)

## Slide 3: Existing Techniques
60 GHz
  Pros
    Huge bandwidth
    Higher resolution (~1.5cm in FMCW)
    Opportunity of fine-grained tracking
  Cons
    Require specialized embedded chip
    Restricted to LOS
Wi-Fi (2.4 GHz, 5 GHz, UWB)
  Pros
    NLOS
    H/W availability more (SDR, USRP, NIC)
    Allows both LOS/NLOS
  Cons
    No fine-grained tracking
    Mostly identify coarse-grained gestures
    Limited bandwidth

## Slide 4: Existing RF based Systems
Name | Technique | Frequency (GHz) | Gesture/Tracking | Accuracy | Range | Hardware | Comments
WiTrack (NSDI ‘14) | FMCW | 5.4-7.25 | 2D Tracking | ~10cm | ~10m | USRP | Custom signal
WiTrack 2.0 (NSDI ‘15) | FMCW | 5.4-7.25 | 2D MU Tracking | ~10cm | ~10m | USRP | Custom signal
WiDeo (NSDI ‘15) | Channel Estimation | 2.4 | Limb Tracking | ~7cm | ~15m | WARP | Multiple APs
WiVi (SIGCOMM ‘13) | ISAR, MUSIC | 2.4 | Motion Tracking | 3 human: 90% | ~7m | USRP | Binary gestures
WiKey (MOBICOM ‘14) | CSI, HMM | 5 | Keystroke | ~85% | ~2m | Intel 5300 | ML based, 2500 pkts/s
WiDraw (MOBICOM ‘14) | CSI, MUSIC | 5 | Hand Tracking | 2D: ~6cm 3D: ~9cm | ~2m of device | Laptop and APs | Initial calibration, ~25 APs
Mudra (CoNext ‘16) | CSI, Nulling, DTW | 2.4 | 9 Finger Gestures | 96% | ~5m | SDR | SDR used, Training free
WiFinger (Mobihoc ‘16) | CSI, Wavelet, DTW | 2.4 | 8 Finger Gestures | 92% | ~4m | USRP | Restricted setup
WiHear (Mobicom ‘15) | MU-MIMO, CSI, Wavelet, DTW | 2.4 | 9 mouth gestures | ~75% | ~8m | USRP, Stepper motor | Restricted, stepper motor calib.

## Slide 5: Things to look for in RF based schemes
Number of Transmitters and Number of Receiver Antennas.
SDR platform (Mudra and its predecessor) or COTS Wi-Fi (WiFinger, WiKey, WiDraw, WiDeo) or Custom setup (WiVi, WiTrack2.0).
Machine learning based or Training Free.
Fine-grained gesture (WiFinger, Mudra), Coarse-grained gesture (WiTrack2.0, WiVi, WiDeo) or 2D/3D tracking (WiDraw) or something else (WiHear - listening, WiKey).
Initial calibration step (WiDraw makes the user move the device for Azimuth and elevation, WiHear rotates the WiFi AP using a stepper motor).
Custom designed signal (FMCW in WiTrack, WiKey - 2500 packets/sec at max rate communication) or in parallel with the communication without hampering it (WiDraw, Mudra).

## Slide 6
Mudra
  Fine grained gesture recognition
  CSI based MIMO nulling
WiDraw
  Hand motion detection
  AoA using CSI
  Hand occlusion of AoA trajectory
WiFinger
  Fine grained gesture recognition
  Unique CSI pattern

## Slide 7: Mudra: User-friendly Fine-grained Gesture Recognition using WiFi Signals
CoNEXT ‘16

## Slide 8: Introduction
Fine grained finger gesture recognition
Utilizes regular WiFi signals
User and Environment Independent
  Training-free
Used CSI to equalize signal utilizing nulling method in 2.4 GHz WiFi
Detects 9 gestures

## Slide 9: System Overview

## Slide 10: System Overview
Equalization
Manual delay addition
Finger movement causes delay mismatch
Subtraction yields troughs

## Slide 11
Finger position sensitive indicator
  Trough location
Trough depth and sensitivity to finger movement depends on Δt
  More Δt : Deeper trough
  More Δt : Less sensitivity

## Slide 12: Gesture Grammar

## Slide 13: Gesture Recognition
Gesture waveforms remain consistent across users at different locations
  Shape is preserved
universal waveform template for each gesture independent of specific user.
Use DTW to match waveform and template

## Slide 14: Setup
NI-based SDR platform
  Two antennas
Distances
  2m LOS
  5m NLOS
Δt is chosen to be 1 (skip one sample)
Gesture performed facing antennas
Metal plate between Tx and Rx to remove direct-path signals

## Slide 15: Results - LOS
Average recognition accuracy is 98%.

## Slide 16: Results - NLOS
Average accuracy is 96%.

## Slide 17
Accuracy is consistent across users
Three users performing simultaneous gestures
  recognition accuracy 94%
  Don’t mention if its for all users or just one

## Slide 18: WiDraw: Enabling Hands-free Drawing in the Air on Commodity WiFi Devices
MobiCom ‘15

## Slide 19: Introduction
Hand motion tracking system using commodity WiFi cards
WiDraw utilizes the
  Channel State Information (CSI) from multiple antennas
  Angle-of-Arrival (AoA)
Harnesses the effect of hand occlusions on the signal strength of incoming signal directions

## Slide 20
Multiple Aps at different locations
  Multiple AoAs
MUSIC using CSI values
  1-D AoA estimates
Notes: we observe that if the user’s hand blocks the signal
arriving along a specific AoA, the AoA’s signal strength will experience
a sharp drop

## Slide 21
Observation:
  If Blocked by hand, AoA’s signal strength experience sharp drop.
  Stays constant otherwise

## Slide 22
Observation:
  Minima when hand is closest to AoA trajectory.
  Drop proportional to hand proximity to the AoA trajectory

## Slide 23: Estimating hand depth
Hand pepth
  distance from hand to the line of Antenna array
Time of minima for each AoA
  t0, t1, t2
α = (t1-t0)/(t2-t0)
Change in depth can be estimated as follows

## Slide 24: Estimate Az and El for each AoA
User rotates RX along Z axis
  Tracks max angle for each AoA
  Max angle used to compute ‘el’
  ‘az’ calculated from ‘el’

## Slide 25: Hand Coordinate Estimation
Minima observed for AoA with azimuth (az) and elevation (el)
yi - hand’s depth from the receiver
Estimated coordinates

## Slide 26
Calculated coordinates may not be exact
  Hand does not occlude the AoA completely
Observation
RSSI drop proportional to Distance between hand and AoA trajectory
RSSI change
  +ve moving away
  -ve moving toward

## Slide 27
Max RSSI drop for one AoA
  Distance from estimated coordinated
Trend of change in RSSI from neighboring AoA
  Resolve ambiguity
Gives true estimate for hand coordinates

## Slide 28: System Architecture

## Slide 29: Setup
AoA values from 30 neighboring transmitters
Atheros 9590 chipset 3 antennas

## Slide 30: 2D Tracking
median tracking error is 5.4 cm
No error accumulation over time

## Slide 31: 3D Tracking
Median tracking error 8.6 cm
Error proportional to depth estimation error

## Slide 32: Results
Using the writing reorganization application - MyScript Stylus

## Slide 33: WiFinger: Leveraging Commodity WiFi for Fine-grained Finger Gesture Recognition
MobiHoc ‘16

## Slide 34: Introduction
Enables fine-grained gesture recognition
  Train &Test CSI pattern across gestures
Resilient to individual diversity and gesture inconsistency
  Once trained can be used for other users
Resilient to environment changes
Works for both LOS & NLOS scenarios
Detects 8 gestures

## Slide 35
Observation
  Each finger gesture has its unique CSI pattern
Gesture recognition
  matching the CSI pattern against the gesture profiles.

## Slide 36: System Architecture

## Slide 37: Multipath Mitigation
Signal components with large time delay removed
  retains the CSI pattern of the finger gesture
  mitigates effect of the changed multipath environment
Remove power delay profile coefficients with delay > 500ns

## Slide 38: Noise Removal
Discrete Wavelet Transform (DWT)
  approximation co-efficients - shape/trend of the signal which retain large scale characteristic
  detail coefficients - high frequency noise and the fine details of the CSI pattern.
Noise removal
  Symlet Wavelet Filter

## Slide 39: Principal Component Identification
Principal Component – invariant part of CSI waveform across the same set of finger gestures that one user performed.
Principal components assigned higher weights when building profiles

## Slide 40: Principal Component Extraction
Extrapolate every sequence to same length
Direct matching samples in the coupling sequence generated by the DTW algorithm are considered as the principal component candidates which represent the consistent gesture segments between two CSI instances.

## Slide 41: Gesture recognition
MD-DTW
  align the CSI pattern to the gesture profiles in the library.
  calculate the similarity between the testing CSI pattern and each of the known gesture profile in the profile library.
Highest and sufficient similarity to the CSI pattern is identified as recognized gesture

## Slide 42: Setup
WiFi device
  Dell LATITUDE E5540 Laptop)
Wireless Access Point
  LINKSYS E2500 N600
10 instances of each gesture to build profiles
User always in between AP and device

## Slide 43: Gesture Grammar

## Slide 44: Recognition Accuracy
Overall recognition accuracy >93%

## Slide 45: Individual Diversity
Trained using 1 user and tested by another
Principal component extraction improves accuracy by over 10%

## Slide 46: Existing RF based Systems
Name | Technique | Frequency (GHz) | Gesture/Tracking | Accuracy | Range | Hardware | Comments
WiTrack (NSDI ‘14) | FMCW | 5.4-7.25 | 2D Tracking | ~10cm | ~10m | USRP | Custom signal
WiTrack 2.0 (NSDI ‘15) | FMCW | 5.4-7.25 | 2D MU Tracking | ~10cm | ~10m | USRP | Custom signal
WiDeo (NSDI ‘15) | Channel Estimation | 2.4 | Limb Tracking | ~7cm | ~15m | WARP | Multiple APs
WiVi (SIGCOMM ‘13) | ISAR, MUSIC | 2.4 | Motion Tracking | 3 human: 90% | ~7m | USRP | Binary gestures
WiKey (MOBICOM ‘14) | CSI, HMM | 5 | Keystroke | ~85% | ~2m | Intel 5300 | ML based, 2500 pkts/s
WiDraw (MOBICOM ‘14) | CSI, MUSIC | 5 | Hand Tracking | 2D: ~6cm 3D: ~9cm | ~2m of device | Laptop and APs | Initial calibration, ~25 APs
Mudra (CoNext ‘16) | CSI, Nulling, DTW | 2.4 | 9 Finger Gestures | 96% | ~5m | SDR | SDR used, Training free
WiFinger (Mobihoc ‘16) | CSI, Wavelet, DTW | 2.4 | 8 Finger Gestures | 92% | ~4m | USRP | Restricted setup
WiHear (Mobicom ‘15) | MU-MIMO, CSI, Wavelet, DTW | 2.4 | 9 mouth gestures | ~75% | ~8m | USRP, Stepper motor | Restricted, stepper motor calib.